## Slide 1
nGenius 3900 Series Packet Flow Switch
For Test Optimization
2017

## Slide 2: Agenda
System overview
Chassis options
Blade options
Transceiver options

## Slide 3: NETSCOUT Test Optimization Solution
TestStreamTM Management Software
Improving Efficiency, Speed, and Performance
in Network and Application Test Labs
Combined L1 switching with L2-4 intelligence
Scalable configurations
Controlled by easy-to-use application software
Save money
Reduce time
Increase utilization
L2-4 INTELLIGENCE
L1 SWITCHING
SCALABLE CONFIGURATIONS

## Slide 4: NETSCOUT Test Optimization Platform
nGenius® 3900 Series Packet Flow Switch
TestStreamTM Management Software
HorizON
HorizON
HIGH SCALABILITY
INTEGRATED INTELLIGENCE
SIMPLE OPERATION

## Slide 5: nGenius 3900 Key Advantages & Features
TestStreamTM Management Software
Integrated Intelligence
  Layer 1 functionality & Layer 2-4 intelligence
  Software-adjustable any-rate blades
  Hybrid electrical and all-optical switching fabrics
High Scalability
  1, 3, and 12 slot chassis options
  Scalable from 16 to 1,152 ports per system
  Distributed and redundant architecture
Simple Operation
  Centralized software control
  Intuitive GUI & 3rd party interoperability
  Instantaneous speed upgrades via software
SCALABLE CONFIGURATIONS

## Slide 6
Test Optimization
Chassis

## Slide 7: nGenius 3900 Series Packet Flow Switch
 | HS-3200 | OS-96 | OS-192 | 3901 |  | 3903 |  | 3912 | 
Total Port Capacity | 32 | 96 | 192 | 10G | 40G | 10G | 40G | 10G | 40G
 |  |  |  | 96 | 24 | 288 | 72 | 1,152 | 288
Slots | N/A | N/A | N/A | 1 |  | 3 |  | 12 | 
Rack Units (RU) | 1 | 3 | 6 | 1 |  | 3 |  | 16 | 
Managed by TestStream Management Software

## Slide 8: HS-3200 Overview
HS-3200 Chassis Features/Specifications | 
32 ports of 40, 100 GbE, 64 ports of 10, 25,50 GbE Switching capacity up to 3.2Tb/s | Operating Environment: (+32° to +104° F)
Fully redundant power supplies | Operating Voltage: (100/260 VAC)
Standalone 19” Rack Mount | Power: 2 x 4.5A @ 120 VAC 2 x 2.9A @ 220 VAC
Max Power: 150 Watts Max using passive cables (ATIS) 398 Watts Max using optical cables (3.5 W/port) | Plug: 2 x NEMA 5-15P (100-240 VAC)
H x W x D: (1 RU) 1.72” x 19.00” x 27.00” | Weight: 24.48 lbs.
32 QSFP28 ports
10,25,40,50,100 GbE
Deterministic Latency to enable accurate test results
Controlled by TestStream Management Software
Ethernet for
Management Software
Redundant Power Supplies/AC Inputs
Fan Assemblies (4)
Redundant Power Supplies/AC Inputs
HS-3200 Features and Benefits
Automated connections are instantaneous and assured
Multimode and Single mode configuration on a per-port basis
Support for 10, 25 40, 50, 100 GbE speeds
Deterministic latency of 540ns
Dual AC power
Front-to-back and back-to-front airflow options
100GbE QSFP28 SR4
40GbE QSFP+ SR4
100GbE QSFP28 LR4
OPTICAL TRANCEIVERS:

## Slide 9: nGenius 3900 OS-192 Overview
192 Duplex Optical Ports (6U)
Redundant Power & Control
Controlled by TestStream Management Software
SM 1260-1675nm
LC Connectors
Redundant
AC Power
Redundant
Multisession
Ethernet
nGenius 3900 OS-192 Features and Benefits
Automated connections are instantaneous and assured
Scalable to 384 SM fiber terminations (192 duplex ports per system)
Single Mode fiber, LC duplex connectors
Data rate and protocol transparent
Dual AC power
Dual Multisession Ethernet and serial communication ports
Circuit confirmation and tracking via software
Near zero latency for time sensitive applications
Reconfiguration of connections in less than 25ms
Direct Beam Steering
nGenius 3900 OS-192 Specifications | 
Scalable: 192 x 192 Fibers | Operating environment: +50° to +104° F / <85% RH N-C
Fully redundant power and control | Operating voltage: 100/240 VAC 50/60 Hz
Standalone 19” rack mount | Power: 2 x 15A @100/240 VAC
H x W x D: 6 RU 10.5” x 19” x 21.7” | Max power: 75W
Weight: 73 lbs. | 

## Slide 10: nGenius 3900 OS-192 Specifications
Parameter | Typical | Max | Units
Insertion Loss | 1.0 | 2.2 | dB
Operating Wavelength Range | 1260 | 1675 | Nm
Parameter | Value
Number of Fiber Ports | 192 Duplex Ports
Fiber Type | Single Mode
Fiber Connection | LC
Loss Repeatability | +/-0.1dB
Connection Stability | +/-0.1dB
Maximum Switching Time | 25ms
Polarization Dependent Loss | <0.1dB
Crosstalk | <-50dB
Return Loss | >50dB
Wavelength Dependent Loss | <0.3dB
Maximum Optical Input Power | 27dBm
Switch Lifetime | >108 Cycles
Dark Fiber Switching | Yes
Bi-Direction Optics | Yes
Operating Temperature | +10°C to +40°C, 85% RH non-condensing
Electrical Power Requirements | Dual 100-240 VAC 50/60 Hz

## Slide 11: nGenius 3900 OS-96 Overview
96 Duplex Optical Ports (3U)
Redundant Power & Control
Controlled by TestStream Management Software
SM 1260-1675nm
LC Connectors
Redundant
AC Power
Redundant
Multisession
Ethernet
nGenius 3900 OS-96 Features and Benefits
Automated connections are instantaneous and assured
Scalable to 96 SM fiber terminations (96 duplex ports per system)
Single Mode fiber, LC duplex connectors
Data rate and protocol transparent
Dual AC power
Dual Multisession Ethernet and serial communication ports
Circuit confirmation and tracking via software
Near zero latency for time sensitive applications
Reconfiguration of connections in less than 25ms
Direct Beam Steering
nGenius 3900 OS-96 Specifications | 
Scalable: 96 x 96 Fibers | Operating environment: +50° to +104° F / <85% RH N-C
Fully redundant power and control | Operating voltage: 100/240 VAC 50/60 Hz
Standalone 19” rack mount | Power: 2 x 15A @110/240 VAC
H x W x D: 3 RU 5.25” x 19” x 21.7” | Max power: 75W
Weight: 41.4 lbs. | 

## Slide 12: nGenius 3900 OS-96 Specifications
Parameter | Typical | Max | Units
Insertion Loss | 1.0 | 2.2 | dB
Operating Wavelength Range | 1260 | 1675 | Nm
Parameter | Value
Number of Fiber Ports | 96 Duplex Ports
Fiber Type | Single Mode
Fiber Connection | LC
Loss Repeatability | +/-0.1dB
Connection Stability | +/-0.1dB
Maximum Switching Time | 25ms
Polarization Dependent Loss | <0.1dB
Crosstalk | <-50dB
Return Loss | >50dB
Wavelength Dependent Loss | <0.3dB
Maximum Optical Input Power | 27dBm
Switch Lifetime | >108 Cycles
Dark Fiber Switching | Yes
Bi-Direction Optics | Yes
Operating Temperature | +10°C to +40°C, 85% RH non-condensing
Electrical Power Requirements | Dual 100-240 VAC 50/60 Hz

## Slide 13: nGenius 3901 Chassis Overview
nGenius 3901 Chassis Features/Specifications | 
Single Blade System Up to 96 ports of 10G, 24 ports of 40G | Operating Environment: (+41° to +104° F)
TestStream Management Software (Embedded or Server) | Operating Voltage: (100/240 VAC)
Standalone 19” Rack Mount | Power : 2 x 15A @ 100/240 VAC
Max Power: 400W | Plug: 2 x NEMA 5-15P
H x W x D: (1 RU) 1.75” x 19.00” x 19.75” | Weight: 20 lbs.
1U / 1-slot
100-240 VAC Input
Controlled by TestStream Management Software
Ethernet for
TestStream Management Software
Redundant AC Power (Alarmed)
(Optional Redundant DC Power Available
Blade Support | Quantity
S-Blade Pro | 1
S-Blade | 1
T-Blade | 1
T100-Blade | 1
Alarmed Fan Assembly
T-Blade
S-Blade
T100-Blade
S-Blade Pro

## Slide 14: System Block Diagram nGenius 3901 Chassis
Blade #1
Switch / Packet Engine
Example: nGenius 3901 Chassis
AC and DC Power
TestStream
Management Software
(Embedded Server)
(Client and CLI)
Chassis
Cooling Fans
SFP
SFP
SFP
SFP
SFP
SFP
(Q)SFP
(Q)SFP
Switch Processor
Embedded MAC
(TestStream Manager)
TestStream
Management Software

## Slide 15: nGenius 3903 Chassis Overview
nGenius 3903 Chassis Features/Specifications | 
Scalable: 1 to 3 Blades (Up to 288 Ports of 10G, 72 ports of 40G) | Operating Environment: (+41° to +104° F)
Fully Redundant Power & Control | Operating Voltage: 100/240 VAC
Standalone 19” rack mount | 
Max Power: 1000W@110 1200W@220 | Power : 2 x 15A @ 100/240 VAC
 | Plug: NEMA 5-15P
 | Plug: C-13
H x W x D: (3 RU) 5.22” x 19.00” x 24.75” | Weight: 50 lbs.
Redundant, Load Sharing
DC power supplies
Redundant AC Power
3U / 3-slot
Redundant Power & Control
Controlled by TestStream Management Software
Redundant Ethernet for TestStream Management Software
Managed / Alarmed
Hot Swappable Fans
Blade Support | Quantity
S-Blade Pro | 3
S-Blade | 3
T-Blade | 3
T100-Blade | 3
T-Blade
S-Blade
T100-Blade
S-Blade Pro

## Slide 16: System Block Diagram nGenius 3903 Chassis with 3 S-Blades
Power Supply 1 (Mgmt 1)
(Client and CLI)
Chassis
Cooling Fans
Blade #1
Switch Engine
TestStream Management Software
(Embedded Server)
SFP
SFP
SFP
Switch Controller
(Primary) Processor
(TestStream Manager)
Blade #2
Switch
Engine
TestStream Management Software
(Embedded Server)
Switch Controller
(Backup) Processor
Blade #3
Switch
Engine
Control
Processor
Blade Processor
Power Supply 2 (Mgmt 2)
Backplane
SFP
SFP
SFP
SFP
SFP
SFP
TestStream
Management Software

## Slide 17: System Block Diagram nGenius 3903 Chassis with 3 T-Blades
Power Supply 1 (Mgmt 1)
Chassis
Cooling Fans
Blade #1
TestStream Management Software
(Embedded Server)
QSFP
SFPs
SFPs
Multi-core Processor
Up to 480 Gbps
Blade #2
TestStream Management Software
(Embedded Server)
QSFP
SFPs
SFPs
Multi-core Processor
Up to 480 Gbps
Blade #3
QSFP
SFPs
SFPs
Multi-core Processor
Up to 480 Gbps
Power Supply 2 (Mgmt 2)
Backplane
720 Gbps
Switch
TestStream Management Software
(Embedded Server)
720 Gbps
Switch
720 Gbps
Switch
SFP = 1/10Gbps, QSFP = 4 x 10Gbps or 1 x 40Gbps
(Client and CLI)
(TestStream Manager)
240 Gbps
up to 480 Gbps
240 Gbps
up to 480 Gbps
240 Gbps
up to 480 Gbps
TestStream
Management Software

## Slide 18: nGenius 3912 Chassis Overview
Hot Swappable Fans Modules
R to L (managed, alarmed)
Hot Swappable SFM Fan Modules
Modular SFM\s
Switch Fabric Module
(up to 8)
nGenius 3912
Chassis Options:
E, 0 SFM
Q, 2 SFM
H, 4 SFM
F, 8 SFM
Cable Management
guides & rack extension ears available
nGenius 3912 Chassis Features/Specifications | 
Scalable: 1 to 12 Blades Up to 1,152 ports of 10G, 288 ports of 40G | Operating Environment: +41° to +104° F
Fully Redundant Power and Control | Operating Voltage: 240 VAC
Standalone 19” Rack Mount | Power: 4 x 16A @ 240 VAC
Max power: 6,000W (Typ.4,200W) | Plug: NEMA L6-20P
H x W x D: (16 RU) + 1RU Clearance Top/Bottom for Airflow 28.00” x 19.00” x 28.00” | Weight: 329 lbs., Fully Loaded
16U / 12-slot
Redundant Power & Control
Controlled by TestStream Management Software
Blade Support | Quantity
S-Blade Pro | 12
S-Blade | 12
T-Blade | 4
T100-Blade | 4
Redundant AC Power
NEMA L6-20P 240 VAC
T-Blade
S-Blade
T100-Blade
S-Blade Pro

## Slide 19
Test Optimization
Blades

## Slide 20: Integrated Intelligence Functions of an Optimized Solution
PACKET GENERATION – Flexible packet generation across 1/10/40/100G interfaces provides initial testing or background load for complex test scenarios.
IMPAIREMENT – Simulate real world network conditions in a test lab environment. Test streams can be manipulated to introduce realistic network anomalies that are not otherwise available without additional tools.
UTILIZATION– Collecting utilization statistics on individual interfaces provides a 3rd party view to corroborate metrics shown by test tools and DUTs. Utilization statistics are available in real time and collected for post-test analysis.
FILTERING – Based on user selectable criteria, test streams are routed at a packet level based on L2-4 header fields. Packets can be routed to specific interfaces or dropped to simulate error conditions.
AGGREGATION – Aggregation creates a single test stream by combining multiple input sources. Combining test streams from application-specific test tools presents a more realistic scenario to the DUT.
RATE CONVERSION – Rate conversion enables you to connect test tools to DUTs regardless of the interface speed. This functionality increases interoperability and greatly extends the lifespan and utilization of 1/10/40/100G test tools.
REPLICATION – Replication allows users to create multiple test streams from a single input source. These replicated streams can be directed to multiple interfaces to increase load on one or more DUTs.
TAP – Passive tapping helps test engineers diagnose problems that occur during test execution. By delivering real-time packet streams to analysis tools, users can analyze and identify problem conditions without disrupting the test traffic flow.
SWITCH – Physical layer switching automates network topology moves, adds, and changes. Connected ports pass unaltered traffic at line rate with no protocol dependencies, optimizing lab operation in a number of ways, including test tool sharing and remote control.
LAYERS 2 – 4
LAYER 1

## Slide 21: nGenius 3900 Series Packet Flow Switch Layer 1-4 Blade Flexibility
Feature | S-Blade Pro | S-Blade | T-Blade | T100-Blade
Speeds Supported | 1/10/40Gbps | 1/10Gbps | 1/10/40Gbps | 10/100Gbps
Protocols Supported | Ethernet | Ethernet, Fibre Channel, SONET | Ethernet | Ethernet
# Full duplex ports per blade | Standard L1 – Up to 72x1/10G or 18x40G Smart L1 – Up to 24x10G or 6x40G | Up to 48 x 1/10G | Up to 48 x 1/10G Up to 4 x 40G | Up to 24 x 10G Up to 2 x 100G
Copper Interface | Yes | Yes | Yes | Yes
MM Fiber Interface | Yes | Yes | Yes | Yes
SM Fiber Interface | Yes | Yes | Yes | Yes
Blade Latency | Standard L1 ports <10ns Smart L1 ports <500ns | <50ns | <500ns | <1,000ns
Blade Height | 1RU | 1RU | 1RU | 1RU
Functions |  |  |  | 

## Slide 22: S-Blade Pro Detail
40G Port status indicators
Internal and external diagnostics
1-slot (24 QSFP ports)
Layer 1 functionality & utilization metrics available on all ports
Ethernet impairment available on smart ports
For use in 3901 and 3903 chassis
Primary or backup controller capable
QSFP
QSFP
1
5
4
8
1/10G Port status indicators
Utilization Statistics
Replication
Layer 1 Switching
Tap
5
1
S-Blade Pro Features
24 QSFP Ports per Blade: Standard L1 – Up to 72x1/10G or 18x40G Smart L1 – Up to 24x10G or 6x40G
Hot-swappable QSFPs with auto speed
Real time and historical Utilization Statistics
Utilization Statistics available on all ports
Media conversion for SM fiber, MM fiber, or copper
Low latency: Standard Layer 1 ports <10ns Smart Layer 1 ports <500ns
Connection Options: Port, group, multi-cast,
Productivity Tools: Port Flap, TAP/test, Port Locking, QSFP Diagnostics
Hot Swappable QSFP, with auto speed and protocol recognition
Multiple speeds and protocols supported
QSFP

## Slide 23: S-Blade Pro Architecture
STANDARD LAYER 1 PORTS
    18 QSFP ports
    Each QSFP 4x1G, 4x10G, 1x40G
    18x40G, 72x1/10G
    <10ns latency
    1/10/40GbE
    *Additional Protocols
BACKPLANE
24 back links
72 back links
Standard L1 front ports
Smart L1 front ports
SMART BRIDGE
  160G
SMART LAYER 1 PORTS
    6 QSFP ports
    Each QSFP 4x10G, 1x40G
    6x40G, 24x10G
    ≈ 500 ns latency
    Ethernet packet ports
    Utilization Statistics
    *Impairment
*See Account Team for details

## Slide 24: S-Blade Detail
SFP
Port status indicators
Hot Swappable SFP and SFP+, with auto speed and protocol recognition
Speeds and protocols selectable by license
Internal and external diagnostics
SFP(+)
S-Blade Layer 1 Features
48 High Density Ports per Blade
Any-Rate Speeds from 1G to 10G on All Ports
Hot-Swappable SFPs with Auto Speed and Protocols
Port, Group, Multi-Cast, Port Flap, TAP or Interactive Test
Media Conversion for SM Fiber, MM Fiber, or Copper
On-Board Data Generator
Low Latency < 50ns
1-slot (48 ports, 1G to 10G on any port)
Layer 1 functionality on all ports
1/10G Ethernet, 1/2/4/8G FC, OC-48-192
Data Generator / any port
for infrastructure verification
Switch
Tap
Replication
Port 1
Port 2
1
2
2
1
SFP
SFP
For use in 3901, 3903, and 3912 chassis
Primary or backup controller capable

## Slide 25: T-Blade Detail
SFP(+)
SFP(+)
1-slot (up to 48 ports, 32-1/10G & 4-40G)
Layer 2-4 functionality on all ports
1/10/40G Ethernet
T-Blade Layer 2-4 Features
48 High Density Ports per Blade (32 SFP+ 4 QSFP+)
Speeds: 32 - 1/10G, 4 - 40G or 48 - 1/10G
Hot-Swappable SFPs - QSFPs
Layer 2-4 Intelligence, All Functions (shown below) on All Ports
Media Conversion for SM Fiber, MM Fiber, or Copper
Deterministic Low Latency (typical <500ns)
Hot Swappable SFP, QSFP, with auto speed and protocol recognition
Port status indicators
1PPS Ports
Packet Generation
Impairment
Traffic Statistics
Filtering
Aggregation
Rate Conversion
Replication
Switch
Tap
QSFP
For use in 3901, 3903, and 3912 chassis
Primary or backup controller capable
Port
Port
1
2
2
1
SFP
SFP

## Slide 26: T100-Blade Detail
T100-Blade Layer 2-4 Features
26 High Density Ports per Blade (24 SFP+ 2 MM CXP)
Speeds: 24 - 10G, 2 - 100G SR10
Hot-Swappable SFPs - CXPs
Layer 2-4 Intelligence, All Functions (shown below) on All Ports
Media Conversion for SM Fiber, MM Fiber, or Copper
Deterministic Low Latency
Port status indicators
Hot Swappable SFP and CXP, with auto speed and protocol recognition
1-slot (26 ports, 24-10G & 2-100G)
Layer 2-4 functionality on all ports
10/100G Ethernet
Internal and external diagnostics
1PPS Ports
SFP(+)
CXP
SFP(+)
CXP
Packet Generation
Impairment
Traffic Statistics
Filtering
Aggregation
Rate Conversion
Replication
Switch
Tap
Port
Port
1
2
2
1
SFP
SFP
For use in 3901, 3903, and 3912 chassis
Primary or backup controller capable

## Slide 27: T100L-Blade Detail
T100-Blade Layer 2-4 Features
26 High Density Ports per Blade (6 QSFP+ 2 SM CFP4)
Speeds: 24 - 10G, 2 - 100G LR4
Hot-Swappable QSFPs - CFP4s
Layer 2-4 Intelligence, All Functions (shown below) on All Ports
Media Conversion for SM Fiber, MM Fiber, or Copper
Deterministic Low Latency
Port status indicators
Hot Swappable CFP4 and QSFP,
With Digital Diagnostics
1-slot (26 ports, 24-10G & 2-100G)
Layer 2-4 functionality on all ports
10/100G Ethernet
Internal and external diagnostics
1PPS Ports
For use in 3901, 3903, and 3912 chassis
Primary or backup controller capable
QSFP(+)
CFP4
QSFP(+)
CFP4
Packet Generation
Impairment
Traffic Statistics
Filtering
Aggregation
Rate Conversion
Replication
Switch
Tap
QSFP

## Slide 28
Solutions/Architecture
Benefits & Licensing

## Slide 29: Scalable 3-Stage Switch Design
Up to 1,152 ports of 10G per system
Up to 288 ports of 40G per system
From 1Gbps to >100Gbps per port
Flexible 1, 3, and 12 slot chassis
Blades interoperate across platforms
High availability
Non-blocking architecture
Central Switch Fabric
L1-4 Application Blades

## Slide 30: Integrated Intelligence
A NETSCOUT solution for testing 10G and 100G DUTs using 1G and 10G tools
Combines Rate Conversion and Aggregation along with Filtering and Tapping, while collecting statistics on all interfaces
10G Test Tool
1G Test Tool
1G Test Tool
10G DUT
1G Analyzer
100G DUT
LAYERS 2 – 4
LAYER 1
Packet Generation
Impairment
Utilization
Filtering
Rate Conversion
Replication
Tap
Switch
Aggregation
FUNCTIONS OF AN OPTIMIZED SOLUTION

## Slide 31: TestStream T-Blade Port Licenses
T-Blades
  Supports 1/10/40G Layer 2-4 Ethernet, all functions on all ports
  32 ports 1/10G and 4 ports 40G or (48 ports 1/10G)
    Each 40G (QSFP) port selectable as 4 x 1/10G
  T-Blade systems :
    3901 & 1 T-Blade 16 x 1/10G ports or 32 x 1/10G and 4 x 40G ports
    3903 & 1 T-Blade 32 x 1/10G and 4 x 40G ports
    T-Blades :
  32 x 1/10G and 4 x 40G ports
    PSL upgrades available in 2 x 40G or 16 x 1/10G ports
Port Licenses
T-Blade
Layer 2-4 PSL
16 x 1/10G
16 x 1/10G & 4 x 40G
Upgrades
16 x 1/10G
2 x 40G
16 x 1/10G
4 x 40G
16 x 1/10G
T-BLADE

## Slide 32: TestStream T100-Blade Port Licenses
T100-Blades and T100L-Blades
  Supports 10/100G Layer 2-4 Ethernet
  All functions on all ports
  24 ports 10G and 2 ports 100G
  T100-Blade systems:
    3901 & 1 T100-Blade 24 x 10G and 2 x 100G ports
    3903 & 1 T100-Blade 24 x 10G and 2 x 100G ports
  T100-Blades:
    24 x 10G and 2 x 100G ports PSL
Port Licenses
T100-Blade
Layer 2-4 PSL
24 x 10G & 2 x 100G
12 x 10G
100GE
12 x 10G
100GE
100GE
100GE
12 x 10G
12 x 10G
T100-Blade
T100L-Blade

## Slide 33: SFP(+) and QSFP+ Options
Test Optimization SFP(+) & QSFP+ Specifications for nGenius 3900 Series Packet Flow Switch |  |  |  |  |  |  |  |  | 
NETSCOUT # | Mktg. Feature | Standard | Fiber / Copper | Wavelength | Line Rate | RX Sens | Rated Distance | Supplier | Supplier P/N
321-1623 | SFP-CT-001 | 10/100/1000 BaseT | Cu | N/A | 10M/100M/1G | N/A | 100m | Avago | ABCU-5710RZ or 40RZ
 |  |  |  |  |  |  |  | Finisar | FCLF-8521-3
321-1624 | SFP-OT-007 | 1/2/4G FC, GigE | 50um MM | 850nm | 1G FC GigE | -20dBm | 550m | Finisar | FTLF8524P2BNV
 |  |  |  |  | 2G FC | -18dBm | 300m |  | 
 |  |  |  |  |  |  |  | Avago | AFBR-57R5APZ
 |  |  |  |  | 4G FC | -15dBm | 150m |  | 
321-1625 | SFP-OT-010 | 1/2/4G FC, GigE | SM | 1310nm | 1G FC GigE | -22dBm | 10km | Finisar | FTL1324P2BTL
 |  |  |  |  | 2G FC | -21dBm | 10km | Avago | AFCT-57R5APZ
 |  |  |  |  | 4G FC | -18dBm | 4km |  | 
321-1626 | SFP-OT-009 | 2/4/8G FC | 50um (OM3)MM | 850nm | 2G FC 4G FC 8G FC | -13dBm -12dBm -11dBm | 500m 380m 150m | Finisar | FTLF8528P2BCV
 |  |  |  |  |  |  |  | Avago | AFBR-57D7APZ
321-1627 | SFP-OT-008 | 10GBASE-SR | 50um (OM3)MM | 850nm | 10GigE | -11dBm | 300m | Finisar | FTLX8571D3BCL
 |  |  |  |  |  |  |  | Avago | AFBR-703SDZ
 |  |  |  |  |  | -7.5dBm |  |  | 
321-1628 | SFP-OT-013 | 10GBase-LR | SM | 1310nm | 10GigE | -10.3dBm | 10Km | Avago | AFCT-701SDZ
 |  |  |  |  |  |  |  | Finisar | FTLX1471D3BCL
T-Blade specific (below) |  |  |  |  |  |  |  |  | 
321-1486 |  | 10GBASE-SR | 50um (OM3)MM | 850nm | 10GigE | -11dBm | 300m | Finisar | FTLX8571D3BCL
 |  |  |  |  |  | -7.5dBm |  | Avago | AFBR-709SDZ
321-1487 |  | 10GBase-LR | SM | 1310nm | 10GigE | -10.3dBm | 10Km | Avago | AFCT-701SDZ
 |  |  |  |  |  |  |  | Finisar | FTLX1471D3BCL
321-0433 |  | 1GE-LX | SM | 1310nm | 1GE | -19dBm | 10Km | Finisar | FTLF1318P3BTL
321-0434 |  | 1GE-TX | Cu | N/A | 10M/100M/1G | N/A | 100m | Finisar | FCLF-8521-3
321-0435 |  | 1GE-SX | MM | 850nm | 1GE | -18dBm | 550m | Finisar | FTLF8519P3BNL
 |  |  |  |  |  | -13.5dBm | 550m | Avago | AFBR-57L5APZ
321-1646 | QSFP+SR4 | 1/10/40GE SR4 | MM | 850nm | 1/10/40GE | -12dBm | 100m | Finisar | FTL410QE2C
 |  |  |  |  | 1/10/40GE | -7.5dBm | 100m | Avago | AFBR79EQDZ
321-1659 | QSFP+LR4 | 40GE LR4 | SM | CWDM | 40GE | -11.5dBm | 10Km | Finisar | FTL4C1QE1C

## Slide 34: NETSCOUT Test Optimization Platform
nGenius® 3900 Series Packet Flow Switch
TestStreamTM Management Software
HorizON
HorizON
HIGH SCALABILITY
INTEGRATED INTELLIGENCE
SIMPLE OPERATION